## Slide 1
RISC-V
LOOP-STREAM DETECTOR
STAVROS STATHOUDAKIS 03512
KONSTANTINOS ANDRIKOPOULOS 03649
STAMOULIS SPYRIDON 03775
University of Thessaly
Parallel Computer Architecture

## Slide 2
Design a stream loop detector
Make it Synthesizable
Integrate it in the RISC-V project
Project Objectives

## Slide 3
→ Job: Monitors the instruction stream.
→ Trigger: Detects a backward branch (B-type or JAL) with a negative immediate value that fits in our cache.
→ Action: Transitions to BUFFERING.
The FSM
STAGE 1: TRACK

## Slide 4
→ Job: Writes each instruction of the loop body into the BRAM.
→ Important Check: If another branch or jump is found inside the loop, it's considered invalid. The FSM aborts and returns to TRACK.
→ Action: When the original branch is reached, transitions to WAIT
The FSM
STAGE 2: BUFFERING

## Slide 5
→ Job: A single-cycle delay state.
→ Purpose: Prepares the BRAM to switch from write mode to read mode.
→ Action: Stalls the instruction fetcher and then transitions to REUSE
The FSM
STAGE 3: WAIT

## Slide 6
→ Job: The main optimization state. Reads instructions from BRAM and feeds them to the pipeline.
→ Action: Blocks the normal instruction fetch stage.
→ Exit Condition: A branch mispredict signals the loop has finished, causing a transition back to TRACK.
The FSM
STAGE 4: REUSE

## Slide 7
The FSM summarized

## Slide 8
Responsible to source the later pipeline stages with stored small loops to be more cycle and power efficient
Implemented using one of Xilinx’s BRAMs.
UOP CACHE
FSM
BRAM

## Slide 9
BRAM operating in SDP mode
Reading and writing using the correct bit and byte-wide enables
32-bit data split across 2 16-bits input and output ports
Reading
Writing
FSM
BRAM

## Slide 10
Post-Implementation Functional Simulation:

## Slide 11
4 extra Instructions
Fixing the reading from BRAM
Because of branch misprediction and the flush that it produces we store 4 wrong instruction in the bram. To solve this we started reading from 4 instructions later. This way we start from the beggining of the loop.

## Slide 12
RISC-V

## Slide 13
RISC-V Execution Codes
CASE 1:
Big Loop with 3 small subloops
CASE 2:
The Biggest Loop to test edge case
CASE 3:
One Instruction Loop to test edge cases
Link for writing assembly code

## Slide 14
CASE 1

## Slide 15
CASE 3

## Slide 16
THANK YOU FOR YOUR ATTENTION
STAVROS STATHOUDAKIS 03512
KONSTANTINOS ANDRIKOPOULOS 03649
STAMOULIS SPYRIDON 03775
University of Thessaly
Parallel Computer Architecture
ANY
QUESTIONS?